District 3

Work Zone Mobility Policy

Significant Route Locations

Permitted Lane Closure Map/List

D3 Studies & Plans

July 27, 2009

Background: Per Safety Engineering Policy 3-07 dated October 12, 2007, the District shall develop a Permitted Lane Closure Map/List for Significant Routes based on Policy 3-07 "Appendix B and District knowledge" for Short Term (3 days or less) lane closures.  Significant Routes are shown in Appendix B and indicate locations on state maintained routes where lane closures are "expected to cause sustained work zone impacts that are not considered tolerable".

Lane closures on Significant Routes of longer than 3 day duration are subject to an Impact Analysis rather than reliance on the Permitted Lane Closure Map/List, per Policy 3-07.

Routes and Strategies: District 3's Significant Routes range from 4-lane interstate highways to 4-lane urban arterials to 2-lane urban and rural arterials. In general, Short Term lane closures on any of the routes should be performed at off peak time periods whenever practical. If the work can be done at night and opened up during daytime hours, the District shall restrict the work to 8 PM -6 AM or a lesser window between those hours, unless approved by the Regional Engineer, or unless there is a municipal objection to night work in residential neighborhoods on an arterial route. On interstate routes, if the work requires constant lane closure of at least 24 hours up to 3 days, an optional alternate route for traffic shall be signed prior to commencing the work.

All applicable short term traffic control standards shall apply.

Holidays: Unless approved by the Regional Engineer, there shall be no Short Term lane closures on Significant Routes during the following holidays or adjacent weekend days (for example, if a holiday falls on a Friday or Monday, the adjacent Saturday and Sunday is also restricted): New Years Day, Easter weekend, Memorial Day, Independence Day, Labor Day, Thanksgiving (2 days), and Christmas. Holiday dates except Easter are to be defined by IDOT's yearly employee holiday calendar.  Other dates may be restricted due to Interstate specific requirements such as:  I-57 move in weekend for the U of I, I-55 and I-80 during race weekends at the Joliet Speedway.

Public Information Plan: when a Significant Route lane closure is within a municipality, a notice shall be sent to the municipality at least 24 hours in advance of the closure.

Significant Route List

Interstates:

I-39 from I-80 to U S. 52

I-57 from IL 17 to the Will County Line

I-80 from IL 89 to the Will County Line

4/5-lane Urban Arterials:

U.S. 34 through Plano

U.S. 45/52 from IL 17 in Kankakee to St. George/Indian Oaks Rd in Bourbonnais

IL 23 from DeKalb to Sycamore

IL 38 west of IL 23 in DeKalb

IL 47 from 1-80 in Morris to Southmor Road s. of Morris

IL 102 through Bourbonnais

IL 23 in North Streator

US 6/IL 23/IL 71 intersection in Ottawa

IL 17 in Kankakee from IL 102 to I-57 in Kankakee

Significant Route List (continued):

2-lane Urban Arterials:

U.S. 34 from WCL Sandwich to 4-lane section in Plano

U.S. 34 from 4-lane section in Plano to IL 25

IL 47 from Kane County line to IL 71 in Yorkville

IL 64 from WCL to ECL in Sycamore

IL 71 from High Point Road to U.S. 34 in Oswego

IL 113 from Will County line to Carbon Hill Road

IL 251 from U.S. 6 in Peru to Oglesby Spur w. of Oglesby

U.S. 24/IL 1 in Watseka from IL 1 W. junction to IL 1 E. junction

U.S. 6 from IL 89 in Spring Valley to IL 351 in La Salle (omit 4-lane section in SV)

U.S. 30 in Kendall County (maintained by District 1 – for information only)

IL 26 from I-80 to U.S. 6 in Princeton

U.S. 34 from IL 251 to I-39 in Mendota

2 Lane Rural Arterials:

IL 1/17 from IL 1 W. junction to NCL Momence

IL 17 from Lehigh Road to 4 lane section in Kankakee

IL 23 from Sycamore to Genoa

IL 47 from IL 71 to Caton Farm Road S. of Yorkville

IL 47 from 4-lane section at Southmor Road to IL 113 N. of Mazon

IL 38 from Lee County line to 4-lane section in DeKalb

IL 38 from 4-lane section at Peace Road in DeKalb to Kane County line

IL 126 from Ridge Road to Will County Line

IL 23 from 4-lane section in South Ottawa to CH 66 S. of Ottawa (Friendship Village road)